## Slide 1
a case study
System to Software Integrity
Matteo Bordin Jérôme Hugues
Cyrille Comar, Ed Falis, Franco Gasperoni,
Yannick Moy, Elie Richa

## Slide 2: How to verify property preservation?
How to combine them?
What about system properties?
Peer review
Testing
Design/Verify-by-contract
(Eiffel, Ada 2012, SPARK, Frama-C, …)
Automatic code generators
Reverse engineering

## Slide 3
a case study
The nose gear challenge

## Slide 4
The ground velocity shall be available iff the data used for computation is no older than 3000ms
The measured velocity shall not differ of more than 3 Km/h from the real velocity during the latest 3000ms

## Slide 5: From System to Software (top-down only)
AADL
System Model
Property 1
Property 2
Property N
…
SPARK 2014
Property 1
Decomposition
Simulink
Property 2
Property N
Code
Generation
SPARK 2014
Property 2
Property N

## Slide 6: From AADL to Simulink and SPARK
Take advantage of AADL mechanisms to
  Describe execution and communication resources (threads, ports, …)
  Bind Simulink or Ada functional models to threads as subprograms
First level of V&V done at model-level
  Interface are correctly typed, behavior correctly defined as subprograms
  Compliance to Ravenscar profile: deterministic concurrency
  Schedulability analysis
  Consistency: WCET of ISR handlers compatible with # of interrupts
subprogram Rotation_Sim
features
Simulated_Velocity : in parameter Velocity;
Click : out event port;
properties
Source_Name => "Rotation_Sim.Rotation_Sim";
Source_Language => (Ada95);
end Rotation_Sim;
thread implementation Rotation_Sensor_Sim.Impl
subcomponents
calls seq : { C : subprogram Rotation_Sim; };
connections
parameter Simulated_Velocity
-> C.Simulated_Velocity;
port C.Click -> Rotation_Click;
end Rotation_Sensor_Sim.Impl;

## Slide 7: From AADL to SPARK
AADL provides full description of use of runtime resources
  Use Ocarina to generate code from architectural description
  Based on archetypes for concurrency, communication
Ada/SPARK compliant, path to high-integrity software
  #5: strong typing, generic, native support for concurrency
  #4: restriction for HI systems
  #3: restrictions for concurrency: Ravenscar profile
  #2: well-known coding patterns
  #1: contracts: pre/post conditions
Functional code integrated as external Ada libraries
  Preserve abstraction boundaries (typing, encapsulation)
  Then connect to integration V&V activities
Compiler checks
100% OK
Best practice
Theorem proving, 90%, on-going

## Slide 8: From Simulink to SPARK 2014
Model-level verification (proof + simulation)
...
if Compare_To_Constant_out1 = estimatedGroundVelocityIsAvailable then
Relational_Operator_out1 := True;
else
Relational_Operator_out1 := False;
end if;
pragma Assert (Relational_Operator_out1);
...
Source-level proof or property preservation
Run-time monitoring of safety properties

## Slide 9: The wrap-up
AADL
System Model
Property 1
Property 2
Property N
…
SPARK 2014
Property 1
Decomposition
Verification by formal proof
Simulink
Property 2
Property N
Verification by simulation
Code
Generation
SPARK 2014
Verification
by formal proof
Property 2
Property N

## Slide 10
TAKE HOME
messages

## Slide 11: Property preservation: how?
Several different techniques
  Peer review, testing, automatic code generation, formal proof, …
How to combine them?
  While providing evidence of coverage
  And taking into account system-level concerns
Use AADL as a pivot representation
  Derive formalized specifications downstream
Rely on languages supporting design-by-contract
  AADL, SPARK, Simulink Assertion Blocks, …
  And translate them across abstraction layers

## Slide 12: Current state & future improvements
SPARK 2014 Formal Verification Toolset
  Currently in Beta, first release in April 2014
Simulink to SPARK 2014 code generator
  Project P, available in Q4 2014
AADL to Ada/SPARK2014 code generator + runtime
  Part of Ocarina distribution, available through http://www.openaadl.org
  Tested with GNATProve GPL 2013

## Slide 13
Cyrille Comar, AdaCore
Ed Falis, AdaCore
Franco Gasperoni, AdaCore
Yannick Moy, AdaCore
Elie Richa, AdaCore
thanks!
Matteo Bordin, bordin@adacore.com
Jérôme Hugues, jerome.hugues@isae.fr